## Slide 1
Session 3
Networking Fundamentals
Understanding how devices talk to each other across a network
S
Lecture by
Shamali Kene
Project Engineer

## Slide 2
AGENDA
Topics Covered
01
TCP/IP Protocol Framework
The rules that govern how data travels across a network
02
IP Address
The unique digital address assigned to every device
03
Subnet Masks
Dividing an IP address into network and host portions
04
CIDR Notation
Flexible, efficient allocation of IP address blocks
Session 3 | Networking Fundamentals
2

## Slide 3
TOPIC 1
TCP/IP Protocol Framework
What is TCP/IP?
TCP/IP is the framework that defines how data moves from one device to another across networks. Transmission Control Protocol / Internet Protocol
It is the set of rules computers use to communicate over a network or the Internet.
Think of it like sending a parcel:
IP → Where should the parcel go?
TCP → Make sure the parcel arrives correctly and in order.
PARCEL
IP addresses it. TCP delivers it —
complete, correct, in order.
TCP/IP =
Transmission Control Protocol /
Internet Protocol
Session 3 | Networking Fundamentals
3

## Slide 4
TOPIC 1
TCP/IP Has 4 Layers
Layer | What it does | Examples
Application | Services applications use | HTTP, DNS, FTP, SSH
Transport | End-to-end communication | TCP, UDP
Internet | Addressing & routing | IP, ICMP
Network Access | Sends data over the network | Ethernet, Wi-Fi
Easy way to remember
Application
Transport
Internet
Network Access
Data flows down to send, and back up to receive.
Session 3 | Networking Fundamentals
4

## Slide 5
A Real Example
Opening a website walks through every layer of TCP/IP
https://google.com
HTTP
Application
Requests the web page content
TCP
Transport
Ensures the page data arrives complete & in order
IP
Internet
Addresses and routes the data to google.com
Ethernet
Network Access
Physically carries the data over the wire / Wi-Fi
Session 3 | Networking Fundamentals
5

## Slide 6
TOPIC 2
IP Addresses
What is an IP Address?
An IP address (Internet Protocol address) is a unique label assigned to every device connected to a computer network. It acts like a digital home address, allowing devices to find and talk to each other.
192.168.1.10
Its unique digital address
Every device on a network — phones, laptops, servers — has one.
Session 3 | Networking Fundamentals
6

## Slide 7
TOPIC 2
Types of IP Addresses
Public IP
Assigned by your internet provider to your entire home or office network. Visible to the whole internet and allows you to access websites.
Private IP
Assigned by your router to individual devices (phone, laptop) inside your local network. Keeps devices safe by hiding them from the public internet.
Dynamic IP
Temporary addresses that change automatically over time. Your internet provider rotates them to save resources — most household devices use these.
Static IP
Permanent addresses that never change. Manually set for servers, business networks, or websites needing a constant, reliable connection.
Session 3 | Networking Fundamentals
7

## Slide 8
TOPIC 2
IPv4 vs IPv6
IPv4
32 bit address
4.3 Billion unique addresses
Format example
192.168.1.1
Disadvantage
Limited number of addresses (only 4.3 billion); not secure.
IPv6
128 bit address
340 Undecillion unique addresses
Format example
2001:db8::1
Disadvantage
Long, hard-to-remember address format.
Session 3 | Networking Fundamentals
8

## Slide 9
TOPIC 3
Subnet Masks
A subnet mask is a 32-bit number used with an IP address to divide it into two parts: the network ID and the host ID.
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
Network portion (24 bits)
Host (8 bits)
Binary 1's → represent the network portion of the IP address. Binary 0's → represent the host portion.
The subnet mask helps a device determine whether another device is on the same local network or a different network — deciding whether communication is direct or must go through a router.
Session 3 | Networking Fundamentals
9

## Slide 10
TOPIC 4
Classless Inter-Domain Routing (CIDR)
CIDR is a method of IP address allocation and routing that allows more efficient use of IP addresses — allocating based on a network prefix rather than a fixed class (A, B, or C).
Why CIDR? — Classful addressing wastes IP addresses
Class | IPs Available | Hosts | Example Wastage
A | 2²⁴ | 2²⁴ − 2 | Too large for small orgs
B | 2¹⁶ | 2¹⁶ − 2 | Wastes 49,150 hosts for 214 needed
C | 2⁸ | 2⁸ − 2 | Small networks only
Problem
Organizations often need a host count that doesn't match class sizes — leading to wastage.
Solution
CIDR allows flexible block allocation matching the exact number of addresses an organization requires — eliminating the fixed-class wastage.
Session 3 | Networking Fundamentals
10

## Slide 11
Thank You
Session 3 · Networking Fundamentals
Shamali Kene | Project Engineer